## Slide 1
Dragonn
Make the Hexagon NPU reachable for models nobody converted for you — and prove, on the laptop itself, that the NPU is really what ran them.
Every number measured
Snapdragon® AI Lab Build & Present Challenge 2026 · Rishi (RishiMaara) · github.com/RishiMaara/Dragonn · MIT
Notes: Hexagon Bridge is a pre-flight check, a conversion pipeline and a real-hardware validation loop for the Hexagon NPU in Snapdragon X PCs. Everything in this deck was measured on a real Snapdragon X Elite.

## Slide 2
A 45 TOPS NPU you cannot reach
Snapdragon X Elite, ASUS Vivobook — for any model outside a vendor catalog
1
The standard recipe quietly costs you
quantize_dynamic() is what every tutorial shows. On a real X Elite it cost MobileNetV2 72 points of accuracy — and crashed the runtime outright on whisper-base.
2
ONNX Runtime hands you a CPU session
The documented providers=[...] argument silently yields CPU-only while your logs say NPU.
3
The chip rejects what every local check passed
One sign bit on one input of one op type: nine LayerNorms refused on silicon, after a clean local run.
Every one of these failures is silent. The app works. The battery doesn't.
Notes: The silent part is what makes this expensive: nothing errors. You ship, and the NPU was never used.

## Slide 3
Four parts, one question
Will this model run on the Hexagon NPU — and did it?
Scanner
Answers it on any Windows PC with no Snapdragon device: static rules first, then Qualcomm's own HTP compiler locally in about 4 seconds. Names the ops and the reason.
Converter
Static a16w8 QDQ the QNN-specific way, calibrated on real data — including the fixes that are not in any quickstart.
Validator
Runs the model on a real Snapdragon X Elite and reconciles the prediction against what the chip actually did.
App
Speech-to-text server and dashboard that report the execution provider that attached, never the one requested.
Built on what already exists: ONNX Runtime's strict no-fallback session, Olive's attention-mask surgery, Qualcomm AI Hub. The missing piece was diagnosis — which failure you have, and which known fix applies.

## Slide 4
Measured on a real Snapdragon X Elite
Qualcomm AI Hub · SC8380XP, Hexagon v73 · every number committed as evidence in models/reports/
17.8 ms
median encoder latency, 100 runs
185 / 187
layers on the NPU — the other two are graph-edge conversions
12.70%
word error rate on CPU, identical to FP32 (14.07% with the encoder on the NPU)
5.2 → 0.5 s
cold vs cached graph load
The silent fallback, priced
A quantized model that misses the NPU runs 26–28% slower than not quantizing at all — measured in two separate sessions on the same device. Quantizing without checking placement is worse than doing nothing.
And the scanner catches what the chip rejects — before you own the chip
The exact model a real X Elite refused is flagged two ways locally: statically, and by running Qualcomm's compiler. Both device logs — the refusal and the acceptance — are committed in the repository.
Notes: AI Hub job links only open for the account owner, so every result is committed as JSON and raw device logs that anyone can read.

## Slide 5
Four traps, stacked
Each one passes every check before it
“Then don't quantize”
The HTP runs float as FP16, and the unquantized encoder compiles into one NPU graph locally. On the device: failed to finalize, error 6000. Twice.
Local SDK 2.50, device 2.45.
The wrong format
Dynamic quantization doesn't reliably cost you the NPU — it reliably costs accuracy. MobileNetV2: 79.5% → 7.2% top-1, with perfect placement.
whisper-base crashed the runtime.
The wrong precision
8-bit activations scan 100% NPU-eligible, compile to one graph, and transcribe gibberish: 93.5% word error rate. 16-bit fixes it.
Placement says nothing about answers.
Only the chip knows
a16w8 scanned clean, measured cosine 0.99 locally — and the X Elite refused all nine LayerNorms because gamma was signed int8.
Unsigned weights: accepted.
Trap 2 was my own claim, corrected: the scanner used to say dynamic quantization means 0% NPU. The device disagreed, so the rule changed.

## Slide 6
It isn't one model
Five popular models, both paths, each profiled on the same X Elite
Model | What it's for | FP32 → naive → this pipeline | On the NPU
MobileNetV2 | Image classification | 79.5% → 7.2% → 79.5% top-1 | 0.36 ms
Whisper-base | Speech recognition | 8.84% → 11.33% → 8.84% WER | 45.7 ms
MiniLM-L6 | Embeddings for local search | 100% → 63.3% → 97.3% same top hit | 1.30 ms
DistilBERT SST-2 | Sentiment | 90.7% → 90.7% → 91.0% | 2.44 ms
CLIP ViT-B/32 | Image search | 98.2% → 98.8% → 98.2% zero-shot | 2.55 ms
Two settings decided four of these five
Weight granularity: per-tensor weights gave MobileNetV2 1.2% top-1 and cost MiniLM a quarter of its search hits — both with flawless NPU placement. Per-channel fixed both, for 0.01 ms. And the exporter, not the quantizer, split every transformer here in two: PyTorch's newer exporter emits GatherND and IsNaN, which the device refused outright (QNN_COMMON_ERROR_MEM_ALLOC). Exported the older way, the same models compiled into one graph and ran.
Notes: MobileNetV2 is the clearest case of the trap: the naive build places perfectly on the NPU and classifies 7% of images correctly. It needs per-channel weights, and nothing in the toolchain tells you.

## Slide 7
Against Qualcomm's own NPU Whisper
Their pre-compiled X Elite build, profiled by me on the same device, through the same harness
Chart: 
| Qualcomm's encoder (FP16) | This pipeline's encoder (a16w8)
Median latency (ms) | 25 | 17.8
2.60 ms
per token — Qualcomm's decoder, 509 of 509 layers on the NPU
The piece this project does not yet run on the NPU. Now measured, not assumed.
What this comparison does and does not say
The two models are not the same graph — Qualcomm restructures attention and stays in float, this pipeline quantizes.
The runs are eight days apart on a shared device pool.
So: a general-purpose quantization path can land in the same league as the vendor's hand-optimised build. Not a benchmark win.

## Slide 8
One command on a Snapdragon laptop
Because “it uses the NPU” should be something you can check, not something you're told
powershell -ExecutionPolicy Bypass -File .\setup-snapdragon.ps1
1
ARM64-native Python
x64 Python under emulation can never load QnnHtp.dll — the NPU is unreachable and nothing says so.
2
The NPU is visible
Registers the plugin properly and reports the devices ONNX Runtime really sees. Names the driver version if it's too old.
3
The model is on it
Builds a session with CPU fallback disabled. If anything would fall back, the session refuses to start.
No Snapdragon hardware needed for the pre-flight check itself — the scanner and the HTP compile check run on any Windows PC.

## Slide 9
Check every number in this deck
Nothing here asks to be taken on trust
The evidence index
models/reports/README.md lists every claim next to the file that backs it — machine-readable results, not prose.
The device's own logs
Raw runtime logs from the runs themselves are committed, including the failures: the chip refusing a model, naming the operator and the error code.
The job IDs
Every measurement carries the profiling job that produced it, so each number traces to one run on one device.
The tests
49 tests, each pinning a bug that once produced a wrong number, run on every push — on Windows with the QNN plugin as well as Linux.
One command
python -m tools.model_zoo rebuilds the five-model comparison from scratch; python -m scanner checks any model you bring.
Scope, precisely: the encoder runs on the NPU and the decoder on CPU in the shipping app — every latency quoted here is an encoder latency.
Notes: The scope line is deliberate: the speedups are encoder speedups, and the deck says so rather than letting a tester discover it.

## Slide 10
Make the NPU checkable
The Hexagon NPU is the reason to buy the laptop. Today it's reachable only for models someone else already converted — and when it isn't reached, nothing tells you. This turns that into a claim you can check for your model, on your machine, in seconds.
6 models
converted and run on a real X Elite
48 tests
each pinning a bug that once gave a wrong number
Every claim
traceable to a committed evidence file
github.com/RishiMaara/Dragonn · MIT · Rishi (RishiMaara)